From: NASA/TM—2010-216246 , A Densified Liquid Methane Delivery System for the Altair Ascent Stage ; Tomsik , et al

TABLE 3.—SOME KEY THERMOPHYSICAL PROPERTIES FOR LIQUID METHANE
Property
Methane
Molecular Weight
16.042 kg/mol
Normal Boiling Point (NBP)
111.7 K
(201.0 °R)
Liquid Density at NBP
442.4 kg/m3
(26.37 lb/ft3)
Triple Point Temperature
90.7 K
(163.3 °R)
Triple Point Pressure
11.72 kPa
(1.70 psia)
Triple Point Liquid Density
451.7 kg/m3
(28.20 lb/ft3)
Solid Methane Density
511.0 kg/m3
(31.90 lb/ft3)
Heat of Fusion
60.7 kJ/kg
(26.10 Btu/lb)
Heat of Vaporization
510.1 kJ/kg
(219.3 Btu/lb)
Slush Density at 50% solids
481.4 kg/m3
(30.05 lb/ft3)
Liquid Viscosity at NBP
1.17×10-4 Pa-s
(7.89×10-5 lb/ft-s)
Liquid Specific Heat at NBP
3.492 kJ/kg-K
(0.834 Btu/lb-°R)
Liquid Thermal Conductivity at NBP
0.188 W/m-K
(0.109 Btu/hr-ft-°R)
J-T Coefficient., Vapor at 293 K
0.00457 K/kPa
(0.0566 o°R/psi)

http://en.wikipedia.org/wiki/Methane_(data_page)

## Vapor pressure of liquid
P in mm Hg	1	10	40	100	400	760	1520	3800	7600	15200	30400	45600
T in °C	–205.9(s)	–195.5(s)	–187.7(s)	–181.4	–168.8	–161.5	–152.3	–138.3	–124.8	–108.5	–86.3	—

Table data obtained from CRC Handbook of Chemistry and Physics 44th ed. Annotation "(s)" indicates equilibrium temperature of vapor over solid. Otherwise temperature is equilibrium of vapor over liquid.

log10 of methane vapor pressure vs. temperature. Uses formula:  given in Lange's Handbook of Chemistry, 10th ed. Note that formula loses accuracy near Tcrit = −82.6°C

http://en.wikipedia.org/wiki/Ethylene_(data_page)
## Vapor pressure of liquid
P in mm of hg	1	10	40	100	400	760	1520	3800	7600	15200	30400
T in °C	–168.3	–153.2	–141.3	–131.8	–113.9	–103.7	–90.8	–71.1	–52.8	–29.1	–1.5	—

Table data obtained from CRC Handbook of Chemistry and Physics, 44th ed.

log10 of ethylene vapor pressure. Uses formula: , obtained from Lange's Handbook of Chemistry, 10th ed.

http://encyclopedia.airliquide.com/images_encyclopedie/VaporPressureGraph/Oxygen_Vapor_Pressure.GIF

http://mcgroup.co.uk/news/2010/2/25/2///Ethylene%20Prices%20Continue%20to%20Rise.html

Looks like price of ethylene is approx 50 cents per pound
http://www.icispricing.com/il_shared/Samples/SubPage128.asp (2010)
Indicative Natural Gas Liquid (NGL) prices – Mont Belvieu, TX
US$/gal	Apr 30	Apr 23	Apr 16	Apr 09
Propane	1.14	1.14	1.13	1.15
Butane	1.56	1.61	1.55	1.48
Isobutane	1.68	1.67	1.60	1.53
Natural Gasoline	2.01	1.98	1.93	1.91
Ethane	0.58	0.59	0.57	0.50
NYMEX Closing	Apr 30	Apr 23	Apr 16	Apr 09
Ethylene Contract ¢/lb	39.00	50.00	66.00	65.00
Ethane Contract ¢/gal	58.02	59.20	56.75	50.22
Crude Oil WTI $/bbl	86.15	85.12	83.24	84.92
Natural Gas $/m Btu	3.92	4.25	4.03	4.07